## Slide 1
Computer Architecture ( VHDL coding) Lab

## Slide 2
There are two portion in VHDL coding.
Entity part: In entity part all inputs, outputs of a hardware circuit and their types are declared.
Architecture part: In architecture part the actual logic is defined.
Basic structure of VHDL programming
VHDL code
entity entity_name is
Port ( port name : in type;
port name : out type);
end entity_name;
architecture Behavioral of entity_name is
Begin
Actual logic;
end Behavioral;
The full form of VHDL
Very High Speed Integrated Circuit
Hardware
Description
Language
For input it is in
For output it is out
Type is either bit or STD_LOGIC
Bit represents either logic 0 or logic 1 only these two logic.
STD_LOGIC represent standard logic ( logic 0, logic1, Uninitialized(U),
Don’t care (X), High Impedance (Z) like different types of logic)
Entity part
Architecture
part
(VHSIC)

## Slide 3: FPGA (Field-Programmable Gate Array)
A field-programmable gate array (FPGA) is an integrated circuit designed to be
configured by a customer or a designer after manufacturing.
Uses for FPGAs cover a wide range of areas—from equipment for video and
imaging, to circuitry for computer, auto, aerospace, and military applications.
FPGA architecture

## Slide 4: FPGA architecture contd.
The three basic types of programmable elements for an FPGA
Configurable logic block (CLB):
An individual CLB consists of a number of discrete logic components itself, such as
look-up tables (LUTs) and flip-flops.
I/O block: Input/output blocks are the components through which data transfers in
to and out of the FPGA.
Programmable interconnect:
Programmable Interconnect Points (PIP) provide the routing paths used to connect
the CLBs and inputs/outputs.
It is a CMOS transistor switch which can be turned on or off by using programming.
Logically these are nothing but MUX and DMUX.

## Slide 5
AND Gate
c= a.b
a
b
c
VHDL code for AND Gate (Dataflow design):
entity andgate is
Port ( a, b : in bit;
c : out bit);
end entity;
architecture Behavioral of andgate is
begin
c<=a AND b;
end Behavioral;

## Slide 6
OR Gate
c= a + b
a
b
c
VHDL code for OR Gate (Dataflow design):
entity orgate is
Port ( a : in STD_LOGIC;
b : in STD_LOGIC;
c : out STD_LOGIC);
end orgate;
architecture Behavioral of orgate is
begin
c<=a OR b;
end Behavioral;

## Slide 7
XOR Gate
a
b
c
c= a + b
VHDL code for XOR Gate (Dataflow design):
entity xorgate is
Port ( a : in STD_LOGIC;
b : in STD_LOGIC;
c : out STD_LOGIC);
end xorgate;
architecture Behavioral of xorgate is
begin
c<=a XOR b;
end Behavioral;

## Slide 8
Half Adder
Half Adder
a
b
s
c
s = a + b
c= a.b
VHDL code for Half adder (Dataflow design):
entity HA is
Port ( a : in STD_LOGIC;
b : in STD_LOGIC;
s : out STD_LOGIC;
c : out STD_LOGIC);
end HA;
architecture Behavioral of HA is
begin
s<=a XOR b;
c<=a AND b;
end Behavioral;

## Slide 9
Full Adder
sf= af + bf + cin
Full Adder
af
bf
sf
cout
cin
cout= af.bf + bf. cin + cin. af
VHDL code for Full Adder (Dataflow design):
entity FA is
Port ( af : in STD_LOGIC;
bf : in STD_LOGIC;
cin : in STD_LOGIC;
sf : out STD_LOGIC;
cout : out STD_LOGIC);
end FA;
architecture Behavioral of FA is
Begin
sf<=af XOR bf XOR cin ;
cout<=(af AND bf) OR (bf AND cin) OR (cin AND af) ;
end Behavioral;

## Slide 10
There are three types of design in VHDL code
Dataflow design
Structural design
Behavioral design
1) Dataflow design: This design is completely logic expression based.
2) Structural design: Here basic building blocks are used to design a new hardware circuit. Like function
3) Behavioral design: This design is completely truth table based.

## Slide 11
Full Adder using two Half Adder
Half Adder
af
bf
sig1
sig2
Half Adder
sf
sig3
cin
cout
Full Adder
VHDL code for Full Adder (Structural design):
entity FA is
Port ( af : in STD_LOGIC;
bf : in STD_LOGIC;
cin : in STD_LOGIC;
sf : out STD_LOGIC;
cout : out STD_LOGIC);
end FA;
architecture Behavioral of FA is
component HA is
Port ( a : in STD_LOGIC;
b : in STD_LOGIC;
s : out STD_LOGIC;
c : out STD_LOGIC);
end component;
signal sig1,sig2,sig3: STD_LOGIC;
begin
HA1:HA port map(af,bf,sig1,sig2);
HA2:HA port map(sig1,cin,sf,sig3);
cout<=sig2 OR sig3;
end Behavioral;
Component
It is like a function prototype
Components are calling here two times.
Here sig1, sig2 and sig3 are intermediate input output which are called signal.

## Slide 12
Ripple Carry Adder
VHDL code for Ripple Carry Adder (Structural design):
entity ripplecarryadder is
Port ( a :in STD_LOGIC_VECTOR (3 downto 0);
b : in STD_LOGIC_VECTOR (3 downto 0);
cin : in STD_LOGIC;
s :out STD_LOGIC_VECTOR (3 downto 0);
cout : out STD_LOGIC);
end ripplecarryadder;
architecture Behavioral of ripplecarryadder is
component FA is
Port ( af : in STD_LOGIC;
bf : in STD_LOGIC;
cin : in STD_LOGIC;
sf : out STD_LOGIC;
cout : out STD_LOGIC);
end component;
signal c : STD_LOGIC_VECTOR (2 downto 0);
begin
fa1:FA port map(a(0),b(0),cin,s(0),c(0));
fa2:FA port map(a(1),b(1),c(0),s(1), c(1));
fa3:FA port map(a(2),b(2),c(1),s(2), c(2));
fa4:FA port map(a(3),b(3),c(2),s(3),cout);
end Behavioral;
a(0)
FA1
b(0)
s(0)
cin
a(1)
FA2
b(1)
s(1)
c(0)
a(2)
FA3
b(2)
s(2)
a(3)
FA4
b(3)
s(3)
cout
c(1)
c(2)
Here VECTOR is used like an array.
3 downto 0 means a is 4 bit binary number ( a(3),a(2),a(1),a(0) )

## Slide 13
Adder-Subtractor composite unit
VHDL code for Adder-Subtractor (Structural design):
entity addsub is
Port ( a : in STD_LOGIC_VECTOR (3 downto 0);
b : in STD_LOGIC_VECTOR (3 downto 0);
sw : in STD_LOGIC;
s : out STD_LOGIC_VECTOR (3 downto 0);
cout : out STD_LOGIC);
end addsub;
architecture Behavioral of addsub is
component FA is
Port ( af : in STD_LOGIC;
bf : in STD_LOGIC;
cin : in STD_LOGIC;
sf : out STD_LOGIC;
cout : out STD_LOGIC);
end component;
FA1
FA2
FA3
FA4
s(0)
s(1)
s(2)
s(3)
sw
cp(0)
cout
cp(1)
cp(2)
a(0)
b(0)
a(1)
b(1)
a(2)
b(2)
a(3)
b(3)
sig(0)
sig(1)
sig(2)
sig(3)

## Slide 14: Adder-Subtractor composite unit contd.
signal sig : STD_LOGIC_VECTOR (3 downto 0);
signal cp : STD_LOGIC_VECTOR (2 downto 0);
begin
sig(0)<=sw XOR b(0);
sig(1)<=sw XOR b(1);
sig(2)<=sw XOR b(2);
sig(3)<=sw XOR b(3);
fa1:FA port map(a(0),sig(0),sw,s(0),cp(0));
fa2:FA port map(a(1),sig(1),cp(0),s(1),cp(1));
fa3:FA port map(a(2),sig(2),cp(1),s(2),cp(2));
fa4:FA port map(a(3),sig(3),cp(2),s(3),cout);
end Behavioral;
FA1
FA2
FA3
FA4
s(0)
s(1)
s(2)
s(3)
sw
cp(0)
cout
cp(1)
cp(2)
a(0)
b(0)
a(1)
b(1)
a(2)
b(2)
a(3)
b(3)
sig(0)
sig(1)
sig(2)
sig(3)

## Slide 15
Multiplexer
I(0)
Multiplexer
4:1
I(1)
I(2)
I(3)
VHDL code for 4:1 Multiplexer (Behavioral design):
entity multiplexer is
Port ( I : in STD_LOGIC_VECTOR (3 downto 0);
S : in STD_LOGIC_VECTOR (1 downto 0);
O : out STD_LOGIC);
end multiplexer;
architecture Behavioral of multiplexer is
begin
Process(I,S)
begin
case S is
when "00" => O<=I(0);
when "01" => O<=I(1);
when "10" => O<=I(2);
when Others => O<=I(3);
end case;
end Process;
end Behavioral;
S(0)
S(1)
O
S(1) | S(0) | O
0 | 0 | I(0)
0 | 1 | I(1)
1 | 0 | I(2)
1 | 1 | I(3)
Truth Table
Process block
within process block execution is sequential
These parameters
are called sensitivity list
switch case

## Slide 16
Demultiplexer
O(0)
DMUX
1:4
O(1)
O(2)
O(3)
VHDL code for 1:4 Demultiplexer (Behavioral design):
entity demux is
Port ( I : in STD_LOGIC;
S : in STD_LOGIC_VECTOR (1 downto 0);
O : out STD_LOGIC_VECTOR (3 downto 0));
end demux;
architecture Behavioral of demux is
begin
process(I,S)
begin
O<="UUUU";
case S is
when "00"=> O(0)<=I;
when "01"=> O(1)<=I;
when "10"=> O(2)<=I;
when others => O(3)<=I;
end case;
end process;
end Behavioral;
S(0)
S(1)
I
S(1) | S(0) | O(3) | O(2) | O(1) | O(0)
0 | 0 | 0 | 0 | 0 | I
0 | 1 | 0 | 0 | I | 0
1 | 0 | 0 | I | 0 | 0
1 | 1 | I | 0 | 0 | 0
Truth Table
Here U means Uninitialized

## Slide 17
Decoder
Decoder
2:4
VHDL code for 2:4 Decoder:
entity decoder is
Port ( a : in STD_LOGIC;
b : in STD_LOGIC;
enable : in STD_LOGIC;
z : out STD_LOGIC_VECTOR (3 downto 0));
end decoder;
architecture Behavioral of decoder is
begin
process(a,b,enable)
variable abar,bbar:STD_LOGIC;
begin
abar:=NOT a;
bbar:= NOT b;
if enable='1'then
z(0)<=abar AND bbar;
z(1)<=abar AND b;
z(2)<=a AND bbar;
z(3)<=a AND b;
else
z<="UUUU";
end if;
end process;
end Behavioral;
z(0)
z(1)
z(2)
z(3)
a
b
enable
a | b | z(3) | z(2) | z(1) | z(0)
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
z(0) = a’ . b’
z(1) = a’ . b
z(2) = a . b’
z(3) = a . b
Here abar, bbar are two variables
Truth Table

## Slide 18: Difference between signal and variable
1. Signal is used to represent intermediate input output which has a real existence.
Variable is used to store the value temporary and not really exist in the hardware circuit.
2. Assigning value to signal and variable is different.
signal s :STD_LOGIC;
s<=‘1’;
variable v : STD_LOGIC;
v:=‘1’;

## Slide 19
VHDL code for Full Adder (Behavioral design):
entity fulbehaviour is
Port ( a : in STD_LOGIC;
b : in STD_LOGIC;
cin : in STD_LOGIC;
s : out STD_LOGIC;
cout : out STD_LOGIC);
end fulbehaviour;
architecture Behavioral of fulbehaviour is
begin
process(a,b,cin)
variable sw: std_logic_vector(2 downto 0);
begin
sw(0):=cin;
sw(1):=b;
sw(2):=a;
case sw is
when "000" => s<='0';cout<='0';
when "001" => s<='1'; cout<='0';
when "010" => s<='1'; cout<='0';
when "011" => s<='0'; cout<='1';
when "100" => s<='1'; cout<='0';
when "101" => s<='0'; cout<='1';
when "110" => s<='0'; cout<='1';
when others => s<='1'; cout<='1';
end case;
end process;
end Behavioral;
a b cin
0 0 0
s cout
0 0
0 0 1
1 0
0 1 0
1 0
0 1 1
0 1
1 0 0
1 0
1 0 1
0 1
1 1 0
0 1
1 1 1
1 1
Truth Table of Full Adder

## Slide 20: Multiplication Using ADD and shift method
A Q Size Comment
0000
0110
4
initialize
0000
0011
3
Right Shift A and Q
1000
0011
3
A+M
1000
0100
0001
2
Right Shift A and Q
1000
1100
0001
2
A+M
0110
0000
1
Right Shift A and Q
0011
0000
0
Right Shift A and Q
M = 8
Q = 6
M = 1000
Q = 0110
Product = 0011 0000

## Slide 21: VHDL code for 4 bit binary multiplier
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use IEEE.STD_LOGIC_arith.ALL;
use IEEE.STD_LOGIC_unsigned.ALL;
entity binary_multiplier is
Port ( m : in STD_LOGIC_VECTOR (3 downto 0);
q : in STD_LOGIC_VECTOR (3 downto 0);
r : out STD_LOGIC_VECTOR (7 downto 0));
end entity;
architecture multiplier of binary_multiplier is
begin
process(m,q)
variable acc: std_logic_vector(8 downto 0);
variable multiplicand:std_logic_vector(4 downto 0);
begin
acc(8 downto 4):="00000";
acc(3 downto 0):=q;
multiplicand:='0' & m;
for i in 1 to 4 loop
if acc(0)='1' then
acc(8 downto 4):=acc(8 downto 4)+ multiplicand;
end if;
acc:='0' & acc(8 downto 1);
end loop;
r<= acc(7 downto 0);
end process;
end multiplier;

## Slide 22: Restoring Division Flow chart
AA = 0; Q = Dividend;
M = Divisor; Size = n
A = A - M
START
END
Left Shift A and Q
Q[0] = 1
Size = Size-1
Size=0 ?
Quotient = Q
Remainder = A
No
No
Yes
Sign of A=0 ?
Yes
Q[0] = 0
A = A + M

## Slide 23: Restoring Division Example
A Q Size Comment
0000
0111
4
initialize
0000
111
4
Left Shift A and Q
1101
4
A=A-M
1101
111
3
Set Q[0]=0 and
A=A+M
0001
3
Left Shift A and Q
1101
A=A-M
1110
0011
2
A=A-M
0000
2
M = 3, Q = 7
M = 0011
-M = 1101
Q = 0111
111
0000
0
3
0011
Set Q[0]=0 and
A=A+M
0011
0001
2
Left Shift A and Q
1
0
0
1101
1
0
0
Set Q[0]=1
0000
1
0
0
1
1
0001
1
Left Shift A and Q
0
0
1
1101
1110
0
0
1
1
A=A-M
Set Q[0]=0 and
A=A+M
0011
0001
0
0
1
0
0
Remainder
Quotient
11
0
11
0
11
0
0

## Slide 24: VHDL code for 4 bit restoring division
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use IEEE.STD_LOGIC_arith.ALL;
use IEEE.STD_LOGIC_unsigned.ALL;
entity division is
Port ( d : in STD_LOGIC_VECTOR (3 downto 0);
m : in STD_LOGIC_VECTOR (3 downto 0);
q : out STD_LOGIC_VECTOR (3 downto 0);
r : out STD_LOGIC_VECTOR (3 downto 0));
end division;
architecture Behavioral of division is
begin
process(d,m)
variable ac:std_logic_vector(7 downto 0);
variable Mbar:std_logic_vector(3 downto 0);
begin
Mbar:=not m;
ac:="0000" & d;
for i in 1 to 4 loop
ac(7 downto 0):=ac(6 downto 0) & 'U';
ac(7 downto 4):=ac(7 downto 4)+Mbar+"0001";
if ac(7)='1' then
ac(0):='0';
ac(7 downto 4):=ac(7 downto 4)+m;
else
ac(0):='1';
end if;
end loop;
q<=ac(3 downto 0);
r<=ac(7 downto 4);
end process;
end Behavioral;

## Slide 25
Thank You